Ford Focus 1.0-LITRE ECOBOOST Specifications

|  |  | 1.0-litre EcoBoost (100, 125PS) |
| --- | --- | --- |
| Type |  | Inline three cylinder turbo petrol, direct fuel injection and Ti-VCT, transverse |
| Displacement | cm3 | 999 |
| Bore | mm | 71.9 |
| Stroke | mm | 82.0 |
| Compression ratio |  | 10.0:1 |
| Max power | PS (kW) | 100 (73.5) | 125 (92) |
|  | at rpm | 6000 | 6000 |
| Max torque | Nm | 170 | 170 (up to 200 with transient overboost) |
|  | at rpm | 1500-4500 | 1500-4500 |
| Valve gear |  | DOHC with 4 valves per cylinder, twin independent variable cam timing |
| Cylinders |  | 3 in line |
| Cylinder head |  | Cast aluminium |
| Cylinder block |  | Cast iron |
| Camshaft drive |  | Low friction Belt-in-Oil with dynamic tensioner |
| Crankshaft |  | Cast iron, 6 counterweights, 4 main bearings |
| Engine management |  | Bosch MED17 with CAN-Bus and individual cylinder knock control |
| Fuel injection |  | High pressure direct fuel injection with 6 hole injectors |
| Emission control |  | Close coupled three-way catalyst system with heated universal oxygen sensor and catalyst monitor sensor post catalyst |
| Emission level |  | Euro Stage 5 |
| Turbocharger |  | Continental low inertia turbo |
| Lubrication system |  | Electronically controlled variable displacement oil pump for improved fuel economy |
| System capacity with filter | litres | 4.1 |
| Cooling system |  | Split cooling system with 2 thermostats |
| System capacity incl heater | litres |  |
| Transmission |  | Durashift 5-speed (iB5) manual | Durashift 6-speed (B6) manual |
| Gear ratios |  |
|  |  | 5th 0.756 4th 0.951 3rd 1.281 2nd 1.926 1st 3.582 Reverse 3.62 FDR 4.25 | 6th 0.690 5th 0.821 4th 1.032 3rd 1.357 2nd 2.048 1st 3.727 Reverse 3.82 FDR 4.07 |

Performance and Economy

|  |  |  | Fuel consumption l/100 km (mpg) | Performance |
| --- | --- | --- | --- | --- |
| Engine | Power (PS) | CO2 (g/km) | Urban | Extra Urban | Combined | Max speed kph (mph) | 0-100 kph 0-62 mph (sec) | 50-100 kph 31-62 mph (sec)* |
| Focus 5-Door |  |
| 1.0 EcoBoost (5-sp man) | 100 | 109 | 5.9 (47.8) | 4.1 (68.8) | 4.8 (58.8) | 185 (115) | 12.5 | 13.2 |
| 1.0 EcoBoost (6-sp man) | 125 | 114 | 6.3 (44.8) | 4.2 (67.3) | 5.0 (56.5) | 193 (120) | 11.3 | 10.8 |
| Focus 4-Door |  |
| 1.0 EcoBoost (5-sp man) | 100 | 112 | 6.0 (47.0) | 4.2 (67.1) | 4.9 (57.6) | 187 (116) | 12.6 | 13.3 |
| 1.0 EcoBoost (6-sp man) | 125 | 117 | 6.4 (44.0) | 4.4 (64.1) | 5.1 (55.3) | 195 (121) | 11.4 | 10.9 |
| Focus Wagon |  |
| 1.0 EcoBoost (5-sp man) | 100 | 112 | 6.0 (47.0) | 4.2 (67.1) | 4.9 (57.6) | 185 (115) | 12.7 | 13.4 |
| 1.0 EcoBoost (6-sp man) | 125 | 117 | 6.4 (44.0) | 4.4 (64.1) | 5.1 (55.3) | 193 (120) | 11.5 | 11.0 |

DIMENSIONS

|  | 5-Door | 4-Door | Wagon |
| --- | --- | --- | --- |
| Dimensions (mm) |  |  |  |
| Exterior |  |  |  |
| Overall length | 4358 | 4534 | 4556 |
| Overall width with/without mirrors | 2010/1823 | 2010/1823 | 2010/1823 |
| Overall width with folded back mirrors | 1858 | 1858 | 1858 |
| Overall max height (unladen) | 1484 | 1484 | 1505 |
| Wheelbase | 2648 | 2648 | 2648 |
| Track front min/max depending on tyre size and wheel offset | 1544/1559 | 1544/1559 | 1544/1559 |
| Track rear min/max | 1534/1549 | 1534/1549 | 1534/1549 |
| Interior |  |  |  |
| Front headroom (without/with sunroof) | 993/977 | 993/977 | 993 |
| Front max legroom (mid-height rearmost seating posn) | 1094 | 1094 | 1094 |
| Front shoulder room | 1411 | 1411 | 1411 |
| Rear headroom (without/with sunroof) | 962/962 | 962/961 | 999 |
| Rear legroom | 849 | 849 | 849 |
| Rear shoulder room | 1336 | 1336 | 1336 |
| Luggage capacity (litres)‡ |  |  |  |
| 5-seat mode, laden to package tray (with full spare) | 277 | 372 | No full size spare |
| 5-seat mode, laden to package tray (with mini spare) | 316 | 421 | 476 |
| 5-seat mode, laden to package tray (with tyre repair kit) | 363 | 475 | 490 |
| 2-seat mode, laden to roof (with full spare) | 1062 |  | No full size spare |
| 2-seat mode, laden to roof (with mini spare) | 1101 |  | 1502 |
| 2-seat mode, laden to roof (with tyre repair kit) | 1148 |  | 1516 |
| Fuel tank capacity (litres) |  |  |  |
| Petrol | 55 | 55 | 55 |

‡Measured in accordance with ISO 3832. Dimensions may vary dependent on the model and equipment fitted.

POWER/TORQUE GRAPHS

100PS FOCUS 1.0-LITRE ECOBOOST

125PS FOCUS 1.0-LITRE ECOBOOST