NEW FORD RANGER – Technical Specifications

Chassis

| Suspension | Front – Double wishbone front suspension with coil-spring |
| --- | --- |
|  | Rear – Berlin eye leaf springs |
| Steering | Type – Electric Power Assisted Steering (EPAS), with rack and pinion gear |
|  | Turning circle (m, Kerb-to-Kerb) – 11.8 (4x2); 12.4 (4x4) |
|  | Turns lock-to-lock – 3.5 |
| Brakes | Front – ventilated discs, 302 x 32 mm |
|  | Rear – drums, 270 x 55 mm (4x2); 295 x 55 mm (4x4) |
|  | Modulation: Standard: Electronic Stability Control (ESC), Traction Control System (TCS), Electronic Brake Assist. ESC system features: Hill Descent Control (HDC), Hill Start Assist (HSA), Trailer Sway Control (TSC), Load Adaptive Control (LAC), Emergency Brake Assist (EBA), Emergency Brake Light (EBL), Roll-Over Mitigation (ROM) |
| Wheels & tyres | Wheel type Wheel size Tyre size | Pressed Steel / Alloy 7.0 x 16-inch 255/70 R 16 | Alloy 8.0 x 17-inch 265/65 R 17 | Alloy 8.0 x 18-inch 265/60 R 18 |
|  | Spare wheel: 16-inch full-size steel spare (18-inch full-size alloy wheel on Wildtrak models) |

Powertrain

| Engine Type | 2.2-litre TDCi 130 PS/96 kW | 2.2-litre TDCi 160 PS/118 kW | 3.2-litre TDCi 200 PS/147 kW |
| --- | --- | --- | --- |
| Capacity (cc) | 2198 | 2198 | 3198 |
| Bore (mm) | 86.0 | 86.0 | 89.9 |
| Stroke (mm) | 94.6 | 94.6 | 100.8 |
| Max power (kW/PS) | 96/130 | 118/160 | 147/200 |
| At engine speed (rpm) | 3700 | 3700 | 3000 |
| Max torque (Nm) | 330 | 385 | 470 |
| At engine speed (rpm) | 1500-2500 | 1500-2500 | 1500-2750 |
| Comp. ratio | 15.7:1 | 15.7:1 | 15.8:1 |
| Cylinders | 4 in line | 4 in line | 5 in line |
| Turbocharger | Fixed geometry turbocharger | Variable geometry turbocharger | Variable geometry turbocharger |
| Fuel injection | High-pressure common-rail with fuel pressure 1800 bar | High-pressure common-rail with fuel pressure 1800 bar | High-pressure common-rail with fuel pressure 1800 bar |
| Emission controls | Coated Diesel Particulate Filter (cDPF) Oxidation catalyst | Coated Diesel Particulate Filter (cDPF) Oxidation catalyst | Coated Diesel Particulate Filter (cDPF) Oxidation catalyst |
| Emission level | Water cooled EGR Euro Stage V | Water cooled EGR Euro Stage V | Water cooled EGR Euro Stage V |
| Transmission |
| Transmission type: | Ford MT82 manual 6-speed | Ford MT82 manual 6-speed | Ford 6R80 automatic 6-speed | Ford MT82 manual 6-speed | Ford 6R80 automatic 6-speed |
| Gear ratios |  |  |  |
| 6th 5th 4th 3rd 2nd 1st Reverse Final Drive | 0.794 1.000 1.223 1.721 2.839 5.441 4.935 3.15 (4x2) 3.15 (4x4) | 0.794 | 0.691 | 0.794 | 0.691 |
|  |  | 1.000 | 0.867 | 1.000 | 0.867 |
|  |  | 1.223 | 1.143 | 1.223 | 1.143 |
|  |  | 1.721 | 1.521 | 1.721 | 1.521 |
|  |  | 2.839 | 2.342 | 2.839 | 2.342 |
|  |  | 5.441 | 4.171 | 5.441 | 4.171 |
|  |  | 4.935 | 3.400 | 4.935 | 3.400 |
|  |  | 3.15 (4x2) | - | - | - |
|  |  | 3.15 (4x4) 3.55 (4x4) optional | 3.73 (4x4) | 3.55 (4x4) | 3.73 (4x4) |

| 4x4 Driveline |
| --- |
| Type | Driver-selectable four-wheel drive with electronically-controlled transfer box offering three modes: Rear-wheel drive (2H) Four-wheel drive high-range (4H) Four-wheel drive low-range (4L) |
| 4x4 Transfer box | Two speed, right hand drop, single offset, aluminium shift-on-the-fly transfer box |
| 4x4 ratios | 1:1 (High Range) 2.48:1 (Low Range) |
| Max. speed when switching | 120 km/h |

Dimensions and capacities

| Exterior (mm) | Single Cab | Super Cab | Double Cab |
| --- | --- | --- | --- |
| Overall length | 5277 | 5362 | 5362 |
| Overall width | 1860 | 1860 | 1860 |
| Overall height unladen | 1800 | 1804 | 1815 |
| Wheelbase | 3220 | 3220 | 3220 |
| Ground clearance | 229 | 229 | 232 |
| Wading depth (4x2) | 800 (600) | 800 (600) | 800 |
| Front track (4x2) | 1560 (1590) | 1560 | 1560 |
| Rear track (4x2) | 1560 (1590) | 1560 | 1560 |
| Front overhang | 905 | 905 | 905 |
| Rear overhang | 1149 | 1226 | 1226 |
| Angles (deg.) |  |  |  |
| Approach angle | 28° | 28° | 28° |
| Departure angle | 28° | 28° | 28° |
| Ramp angle | 25° | 25° | 25° |
| Interior (mm) |  |  |  |
| Front (mm) |  |  |  |
| Headroom | 1024 | 1024 | 1022 |
| Max. leg room | 1058 | 1058 | 1058 |
| Shoulder room | 1437 | 1437 | 1440 |
| Rear (mm) |  |  |  |
| Headroom | - | 938 | 975 |
| Max. legroom | - | 796 | 902 |
| Shoulder room | - | 1400 | 1430 |
| Cargo Bed (mm) |  |  |  |
| Width | 1560 | 1560 | 1560 |
| Width between arches | 1139 | 1139 | 1139 |
| Length | 2317 | 1847 | 1549 |
| Depth | 511 | 511 | 511 |
| Loading height | 835 (724) | 835 | 835 |

Weights

Note:  Sample data provided for selected U.K. market specification vehicles.

Please contact your local representative for details of specific models within each market.

| Versions | Final drive ratio | Minimum kerbweight (kg) | Gross Vehicle Mass (kg) | Maximum Gross Payload (kg) | Max. towable mass (kg) |
| --- | --- | --- | --- | --- | --- |
| Single Cab |  |  |  |  |  |
| 2.2L TDCi 160 PS 4x4 XL | 3.15 | 1931 | 3200 | 1269 | 1800 (750) |
| 2.2L TDCi 160 PS 4x4 XL | 3.55 | 1933 | 3200 | 1267 | 3500 (750) |
| Super Cab |  |  |  |  |  |
| 2.2L TDCi 160 PS 4x4 XL | 3.15 | 1970 | 3200 | 1230 | 1800 (750) |
| 2.2L TDCi 160 PS 4x4 XL | 3.55 | 1970 | 3200 | 1230 | 3500 (750) |
| Double Cab |  |  |  |  |  |
| 2.2L TDCi 160 PS 4x4 Limited | 3.15 | 2102 | 3200 | 1098 | 1800 (750) |
| 2.2L TDCi 160 PS 4x4 automatic Limited | 3.73 | 2119 | 3200 | 1081 | 3500 (750) |
| 3.2L TDCi 200 PS 4x4 Limited | 3.55 | 2150 | 3200 | 1050 | 3500 (750) |
| 3.2L TDCi 200 PS 4x4 automatic Limited | 3.73 | 2167 | 3200 | 1033 | 3500 (750) |

Minimum kerbweight represents the lightest kerbweight including full fluid levels and 90 per cent fuel levels, subject to manufacturing tolerances and options, etc. fitted. XLT, Limited and Wildtrak models will have greater kerb masses and, therefore, lower payloads due to the increased amount of standard equipment.

Towing limits quoted represent the maximum braked towing capacity of the vehicle on a 12 per cent gradient at sea level – unbraked towing capacities in brackets.

The performance and economy of all models will be reduced when used for towing. 80 kg roof load for all versions. 220 kg nose weight limit for all versions.

Economy, Performance and Emissions

Note:  Sample data provided for selected U.K. market specification vehicles.

Please contact your local representative for details of specific models within each market.

|  | Fuel consumption l/100 km (mpg) | PerformanceØ |
| --- | --- | --- |
|  | CO2 emissions (g/km)ØØ | Urban | Extra Urban | Combined | Max. speed km/h (mph) | 0-100 km/h (0-62 mph) secs |
| Single Cab |  |
| 2.2 Duratorq TDCi (160 PS) 4x4, Final Drive 3.15 | 177 | 7.3 (38.7) | 6.4 (44.1) | 6.7 (42.2) | 175 (109) | 11.8 |
| 2.2 Duratorq TDCi (160 PS) 4x4, Final Drive 3.55 | 191 | 8.3 (34.0) | 6.7 (42.2) | 7.3 (38.7) | 175 (109) | 11.8 |
| Super Cab (inc. XL, XLT and Limited) |  |
| 2.2 Duratorq TDCi (160 PS) 4x2, Final Drive 3.15 | 177 | 7.7 (36.7) | 6.3 (44.8) | 6.7 (42.2) | 175 (109) | 11.8 |
| 2.2 Duratorq TDCi (160 PS) 4x4, Final Drive 3.15 | 171 | 7.1 (39.8) | 6.1 (46.3) | 6.5 (43.5) | 175 (109) | 11.8 |
| 2.2 Duratorq TDCi (160 PS) 4x4, Final Drive 3.55 | 185 | 8.2 (34.4) | 6.6 (42.8) | 7.1 (39.8) | 175 (109) | 11.8 |
| Double Cab (inc. XL, XLT, Limited and Wildtrak) |  |
| 2.2 Duratorq TDCi (160 PS) 4x4, Final Drive 3.15 | 171 | 7.1 (39.8) | 6.1 (46.3) | 6.5 (43.5) | 175 (109) | 11.8 |
| 2.2 Duratorq TDCi (160 PS) 4x4, Final Drive 3.55 | 185 | 8.2 (34.4) | 6.6 (42.8) | 7.1 (39.8) | 175 (109) | 11.8 |
| 2.2 Duratorq TDCi (160 PS) 4x4 automatic, Final Drive 3.73 | 209 | 9.6 (29.4) | 7.0 (40.4) | 8.0 (35.3) | 175 (109) | 12.8 |
| 3.2 Duratorq TDCi (200 PS) 4x4, Final Drive 3.55 | 218 | 9.7 (29.1) | 7.4 (38.2) | 8.3 (34.0) | 175 (109) | 10.9 |
| 3.2 Duratorq TDCi (200 PS) 4x4 automatic, Final Drive 3.73 | 234 | 11.4 (24.8) | 7.4 (38.2) | 8.9 (31.7) | 175 (109) | 10.6 |

ØFord test figures. ØØThe declared Fuel/Energy Consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

# # #

About Ford Motor Company

Ford Motor Company is a global automotive and mobility company based in Dearborn, Mich. With about 199,000 employees and 67 plants worldwide, the company’s core business includes designing, manufacturing, marketing, financing and servicing a full line of Ford cars, trucks, SUVs and electrified vehicles, as well as Lincoln luxury vehicles. At the same time, Ford is aggressively pursuing emerging opportunities through Ford Smart Mobility, the company’s plan to be a leader in connectivity, mobility, autonomous vehicles, the customer experience and data and analytics. For more information regarding Ford, its products worldwide or Ford Motor Credit Company, visit www.corporate.ford.com.

Ford of Europe is responsible for producing, selling and servicing Ford brand vehicles in 50 individual markets and employs approximately 53,000 employees at its wholly owned facilities and approximately 68,000 people when joint ventures and unconsolidated businesses are included. In addition to Ford Motor Credit Company, Ford Europe operations include Ford Customer Service Division and 24 manufacturing facilities (16 wholly owned or consolidated joint venture facilities and 8 unconsolidated joint venture facilities). The first Ford cars were shipped to Europe in 1903 – the same year Ford Motor Company was founded. European production started in 1911.